## Slide 1
ECE4078 Intelligent robotics
Lab 2-2: Extended Kalman Filter
AI art generated by https://www.craiyon.com/
(prompt: “a penguin robot shopping for fruits and vegetables in a supermarket”)

## Slide 2
Week | Objectives | Milestones
1: C1-1 | Introduction and setup | 
2: M1-1 | Calibration, ARUCO markers | C1 due
3: M1-2 | SLAM | 
4: M1-3 | SLAM | 
5: M2-1 | Object recognition & localisation | M1 due
6: M2-2 | Object recognition & localisation | 
7: M3-1 | Navigation & Planning | M2 due
8: M3-2 | Navigation & Planning | 
9: C2 | Integration & Improvement | M3 due
10: Final | Trial run of final demo | C2 due
11: Final | Final demo | Final demo due
12: No lab | N/A | N/A
ECE4078 Intelligent robotics
*

## Slide 3
Recap
M2: SLAM
Your task is to estimate the position of all ARUCO markers within the arena
Task 1: Wheel calibration (Week 2)
- Objective is to calculate the wheel radius and the distance between both wheels
Task 2: Camera calibration (Week 2)
- Objective is to calculate the intrinsic parameters of the camera
Task 3: SLAM (Week 3 & 4)
- Estimate the position of markers in the environment using an Extended Kalman filter (EKF)
- Two main files to modify:
- “slam/ekf.py”: “predict()” and “update()” functions
- “slam/robot.py”: “derivative_drive()” and “covariance_drive()” functions
- Your solution should automatically generate “lab_output/slam.txt” for evaluation

## Slide 4
Extended Kalman filter
When to use a Kalman filter:
- Sensor fusion
- Want to apply dynamics + sensor measurements
There are two main steps
1: Prediction step – We apply a dynamic model to estimate what the state should look like
given our previous state. Eg: Knowing the velocity of an object, we can guess what it’s position will be 1 second into the future
2: Update step – Correcting / updating the estimate of the current state with observations from sensor readings
Eg: We use a GPS to get a direct observation of what the position actually is
But how much should we “update” our state given an observation?
What if we have multiple sensors (Camera/GPS/LIDAR), which one should we use?
Kalman filters are a probabilistic algorithm to estimate a given state (i.e. mean and covariance)
- If we are confident in our dynamic model, then we shouldn’t rely heavily on noisy observations
- If we have a noisy sensor (GPS), then we should weight it less than an accurate one (LIDAR)

## Slide 5
Hints
Before trying to implement your Kalman filter by modifying ekf.py & robot.py have a read of all the functions currently in these files as you can use them to compute some of the matrices (ESPECIALLY the drive function in robot.py)
Don’t forget to call the self.set_state_vector function inside ekf.py to update the state estimate
You can create your own arena by crafting your own marker blocks (see “Week02-04 /diy_prints ”) and making a physical arena.
A map generator (see “image_to_map_generator” under root) is provided to help you generate true maps for evaluating your SLAM in a physical arena. DON’T USE IT TO CHEAT.
Check out the additional contents in Lab2_additional_contents.pptx, including an EKF example and optional improvements